## Slide 1
WORKSHOP ON BRAIN-MACHINE INTERFACES IEEE SMC 2026 October 4-7, 2026
Towards Enhanced Information Transfer Rates in SSVEP-Based BCIs Using
Conway's Game of Life as Visual Overlay
Atilla Cantürk and Ivan Volosyak
Faculty of Technology and Bionics
Rhine-Waal University of Applied Sciences, 47533 Kleve, Germany

## Slide 2
The Problem
High-contrast flickering targets cause visual fatigue and eye strain [1,2]
Reduced vigilance degrades SSVEP amplitude and classification accuracy
Repetitive tasks reduce attentional engagement during prolonged gaze fixation
Proposed Solution
Augment SSVEP targets with a dynamic visual overlay
Conway's Game of Life: complex evolving patterns from four simple rules
Phase-lock GoL dynamics to SSVEP flicker → no change to decoding
Hypothesis: richer visual context sustains attention while maintaining performance
Motivation
For assistive end users who rely on a BCI daily,
comfort and engagement decide long-term acceptance.
[1] T. Cao, F. Wan, C. M. Wong, J. N. da Cruz, and Y. Hu, "Objective evaluation of fatigue by EEG spectral analysis in steady-state visual evoked potential-based brain-computer interfaces,“ BioMedical Engineering OnLine, vol. 13, no. 1, Mar. 2014.
[2] M. Azadi Moghadam and A. Maleki, "Fatigue factors and fatigue indices in SSVEP-based brain-computer interfaces: a systematic review and meta-analysis," Frontiers in Human Neuroscience, vol. 17, Nov. 2023.

## Slide 3
Background
Chen et al. 2023; Volosyak et al. 2011
Higher frequencies / lower contrast mitigate fatigue while largely preserving decoding performance
Fodor & Volosyak 2025
Imperceptible VEP (I-VEP): above critical fusion threshold
eliminates flicker perception, retains separability
StAR-Burst: random texture patches on flicker targets; modifying visual composition preserves performance and improves UX
Dehais et al. 2024
Gabor-based textured flickers maintain strong decoding and improve comfort (J Neural Engineering)
Schrag et al. 2025
Textured SSVEP stimuli affect comfort in pediatric BCI
but clear gains in neural response are inconsistent
Gap: Application of a dynamic textured stimuli to improve SSVEP BCI
classification not yet tested.
Gomel et al. 2025 (SMC)

## Slide 4
Conway's Game of Life
1
Underpopulation
Live cell with < 2 live neighbours → dies
2
Survival
Live cell with 2 or 3 neighbours → lives
4
Overpopulation
Live cell with > 3 neighbours → dies
3
Reproduction
Dead cell with exactly 3 neighbours → born
Invented by John Conway (1970)
Grid of cells: alive or dead, evolving step by step
No player input → everything follows four simple rules

## Slide 5
PC
Dell Precision, Intel Core i9 (5.3 GHz), RTX-3070
OS
Windows 11 Education (24H2)
Monitor
Acer Nitro XV25Q F — 1920×1080, 240 Hz
EEG Amplifier
g.USBamp (Guger Technologies, Schiedlberg, Austria)
EEG Channels
PO7, PO3, POz, PO4, PO8, O1, Oz, O2 (10-10 system)
Reference / GND
Cz / AFz | Impedance < 5 kΩ (abrasive gel)
Sampling Rate
600 Hz
Hardware - Setup

## Slide 6
3-step SSVEP speller with GoL overlay
3-Step SSVEP Speller
4 stimulus boxes (230×230 px) in 1×4 matrix
Frequencies: 6.67, 7.5, 8.57, 10 Hz
26 letters + underscore across 3 letter-group boxes
4th box: UNDO / backspace function
Audio + visual (green/red) feedback on selection
Experimental Design
Within-subject design: Condition 1 (default) vs Condition 2 (GoL overlay)
Starting condition counterbalanced across participants
3 spelling tasks: RELAX, HAVE_FUN, KEEP_BEING_REAL_OUTSIDE
~15–20 min per condition + short rest break between
No classifier training required — training-free FBCCA

## Slide 7
The GoL overlay
Condition 1 — Default Stimuli
4 boxes, white ↔ black alternation at assigned frequency
Full contrast, no additional overlay
No GoL simulation running
Condition 2 — GoL Overlay
Identical boxes and frequencies — only overlay added
128×128 cellular automaton grid per box
GoL state updated at every white↔black transition (phase-locked to flicker)
Active cells rendered at mid-contrast: grey on white; invisible on black
Seed: sparse random (p ≤ 0.10) + predefined library patterns

## Slide 8
Overlay Comparison
Default Stimuli
▶
GoL Overlay
▶
vs

## Slide 9
Classification
Filter Bank Decomposition
5 sub-bands, 2nd-order Butterworth bandpass
FB₁: 6–60 Hz | FB₂: 14–60 Hz
FB₃: 22–60 Hz | FB₄: 30–60 Hz
FB₅: 38–60 Hz
Upper cut-off 60 Hz = g.USBamp maximum
Weights: wᵢ = (i+1)⁻¹·²⁵ + 0.25
emphasises lower-frequency sub-bands
Decision Criteria
Sliding 3.0 s window, updated every 50 ms (20 Hz update rate)
Classify if: ≥ 1.5 s elapsed AND Δscore ≥ 0.15
1 s gaze-shift delay after each accepted classification
Reference signals: sine/cosine at fundamental + 5 harmonics per frequency
No subject-specific classifier training

## Slide 10
Participants (N = 6)
5 male, 1 female; (22.83 ± 2.93 years)
3/6 prior BCI experience;
1/6 knew Conway's GoL
No neurological/psychiatric conditions (self-report)
Written consent (Declaration of Helsinki)
Ethics approval 24-11957-BO
No classifier training performed
Procedure
Pre-questionnaire.
Calibration.
Condition A (~15–20 min):
  RELAX
  HAVE_FUN
  KEEP_BEING_REAL_OUTSIDE
Rest break between conditions
Condition B: alternate stimulus condition
Post-questionnaire
Participants and Procedure

## Slide 11
Performance - Accuracy
97.4%
GoL Disabled
95% CI: [94.4, 100]
95.6%
GoL Enabled
95% CI: [92.4, 98.8]
−1.8 pp
Difference
N=6 pilot — overlapping CIs
Chart: 
| RELAX | HAVE_FUN | KEEP_BEING_ REAL_OUTSIDE
GoL Disabled | 100 | 97.64 | 94.58
GoL Enabled | 98.14 | 95.08 | 93.61

## Slide 12
Performance - ITR
40.95
bits/min
GoL Disabled
95% CI: [29.19, 52.70]
34.53
bits/min
GoL Enabled
95% CI: [21.33, 47.73]
−6.42
bits/min
Difference
Wide overlapping CIs
Chart: 
| RELAX | HAVE_FUN | KEEP_BEING_ REAL_OUTSIDE
GoL Disabled | 47.8 | 42.34 | 32.7
GoL Enabled | 38.15 | 33.35 | 32.09

## Slide 13
Discussion
Questionnaire Results (n=6)
Preference: 50% preferred default, 50% preferred GoL overlay
Fatigue: 2.33 ± 0.82 → 4.00 ± 1.26 (Δ = +1.67 Likert points)
Device control feasibility: median 2 (IQR 1–4); 66.7% agreement
Interesting: all participants preferring GoL showed lower accuracy + ITR under GoL
Discussion
Accuracy remained high (97.4% vs 95.6%), GoL did not break SSVEP detection
ITR decrease likely due to increased visual complexity → reduced fixation stability, more eye-movement artifacts
Pilot (N=6): too small for definitive conclusions - effect directions, not significance
Results differ from Dehais 2024 textured flicker - different overlay dynamics, task design, metrics

## Slide 14
Conclusion
Objective:
Evaluated a novel stimulus augmentation approach: embedding dynamic Conway's GoL overlay onto SSVEP flicker targets
Accuracy remained high in both conditions; ITR was lower with the overlay under the tested parameters
Future Goals:
Larger participant pool (N > 6) with novice BCI users
Systematically vary overlay density, contrast, and update coupling rate
Test GoL overlay with cVEP paradigm; explore GoL-driven SSMVEP
Separate analysis of decision time vs decoding accuracy to isolate the overlay's effect

## Slide 15
https://bci-lab.hochschule-rhein-waal.de
Our Team
Projects
Tools
List of publications
Contacts
Atilla Cantürk Ivan Volosyak
Thank You – Q & A

## Slide 16
References
[1] J. R. Wolpaw et al., "Brain–computer interfaces for communication and control," Clin. Neurophysiol., vol. 113, no. 6, pp. 767–791, 2002.
[2] M. Nakanishi et al., "Enhancing detection of SSVEPs for a high-speed brain speller using task-related component analysis," IEEE TBME, vol. 65, no. 1, pp. 104–112, 2018.
[3] M. Azadi Moghadam and A. Maleki, "Fatigue factors and fatigue indices in SSVEP-based BCIs: a systematic review and meta-analysis," Front. Hum. Neurosci., vol. 17, 2023.
[4] T. Cao et al., "Objective evaluation of fatigue by EEG spectral analysis in SSVEP-based BCIs," BioMed. Eng. OnLine, vol. 13, no. 1, 2014.
[5] M. A. Fodor and I. Volosyak, "Towards visual-fatigue-free BCI with imperceptible visual evoked potentials (I-VEP)," IEEE SMC, pp. 3813–3818, 2025.
[6] X. Chen et al., "Optimizing stimulus frequency ranges for building a high-rate high frequency SSVEP-BCI," IEEE TNSRE, vol. 31, pp. 1277–1286, 2023.
[7] I. Volosyak et al., "BCI demographics II: how many (and what kinds of) people can use a high-frequency SSVEP BCI?," IEEE TNSRE, vol. 19, no. 3, pp. 232–239, 2011.
[8] P. Stawicki and I. Volosyak, "Comparison of modern highly interactive flicker-free SSMVEPs for practical BCIs," Brain Sci., vol. 10, no. 10, p. 686, 2020.
[9] V. Bravou and A. Drigas, "BCI-based games and ADHD," Res. Soc. Dev., vol. 10, no. 4, p. e52410413942, 2021.
[10] J. Gomel et al., "Pre-decision feedback in code-modulated visual evoked potentials BCI for an 11-class keypad typing task," IEEE SMC, pp. 3800–3805, 2025.
[11] F. Dehais et al., "Leveraging textured flickers: a leap toward practical, visually comfortable, and high-performance dry EEG code-VEP BCI," J. Neural Eng., vol. 21, no. 6, p. 066023, 2024.
[12] M. Gardner, "Mathematical games," Scientific American, vol. 223, no. 4, pp. 120–123, 1970.
[13] I. Volosyak et al., "Towards solving of the illiteracy phenomenon for VEP-based BCIs," Biomed. Phys. Eng. Express, vol. 6, no. 3, p. 035034, 2020.
[14] X. Chen et al., "Filter bank canonical correlation analysis for implementing a high-speed SSVEP-based BCI," J. Neural Eng., vol. 12, no. 4, p. 046008, 2015.
[15] E. Schrag et al., "An investigation into the comfort and neural response of textured visual stimuli in pediatric SSVEP-based BCI," Sci. Rep., vol. 15, no. 1, p. 26168, 2025.
[16] ConwayLife.com, "Conway's Game of Life pattern collection," conwaylife.com/patterns/, accessed 17 Feb. 2026.