## Slide 1
WORKSHOP ON BRAIN-MACHINE INTERFACES IEEE SMC 2026
October 4-7, 2026
SSVEP Chess: A Brain-Controlled
Illuminated Puzzle Board
Atilla Cantürk and Ivan Volosyak
Faculty of Technology and Bionics
Rhine-Waal University of Applied Sciences
47533 Kleve, Germany
Notes: Hello, and thank you for joining this session. My name is Atilla Cantürk, and I will be presenting our work titled "SSVEP Chess: A Brain-Controlled Illuminated Puzzle Board." This is joint work with Professor Ivan Volosyak at the Faculty of Technology and Bionics, Rhine-Waal University of Applied Sciences, in Kleve, Germany. Over the next ten minutes I will walk you through the motivation for this system, how it was built, how we evaluated it, and what we learned.

## Slide 2
Motivation
Where SSVEP stops working
Several decades of SSVEP research, still almost no everyday use
Long setup, low acceptance, accuracy that drops the moment you leave the lab
Offline benchmarks replay recorded data — they cannot fail the way a live system fails
So: does SSVEP survive contact with a real task?
A practical application of SSVEP
Flickering stimuli built into a real, physical chess board
The user plays an actual game — not a screen-based demo
SSVEP as a working product, not a laboratory paradigm
A game is a demanding benchmark
Time pressure and shifting attention, like real use
Objective success criterion: the intended legal move, or not
Chess rules narrow the possible choices
Measures UX alongside accuracy: fatigue, frustration, control

## Slide 3
Brain-Computer Interface (BCI):
Translates brain activity into control or communication signals in real time, bypassing normal muscular pathways
Steady-State Visual Evoked Potential (SSVEP):
Oscillatory response of the visual cortex when a user gazes a target flickering at a constant frequency
Each target is tagged with its own frequency, so the attended target is decoded from the EEG spectrum
High information transfer rate (ITR), little user training, robust across users → widely used in BCI applications (spellers and control applications)
Flickering Stimulus (e.g. 10 Hz)
Gaze Fixation
Visual Cortex Response (EEG at Oz)
SSVEP: spectral peak at 10 Hz
J. R. Wolpaw et al., “Brain–computer interfaces for communication and control,” Clin. Neurophysiol., vol. 113, no. 6, pp. 767–791, 2002.
F.-B. Vialatte et al., “Steady-state visually evoked potentials: Focus on essential paradigms and future perspectives,” Prog. Neurobiol., vol. 90, no. 4, pp. 418–438, 2010.
SSVEP BCIs

## Slide 4
SSVEP Chess State Machine
①
Board State
Legal moves determine which squares are activated
②
LED Flicker
Each active square gets a unique SSVEP frequency
③
EEG Capture
8-channel occipital EEG, 512 Hz, g.USBamp
④
FBCCA Decode
Confidence-thresholded; no-decision if below gap
⑤
Chess Action
Move executed; board updated; cycle repeats
Only chess-legal squares are activated → smaller, dynamic target set per move → improved classification reliability

## Slide 5
Chessboard Specifications
Board size
46 cm × 46 cm, 64 cells (5.75×5.75 cm² each)
LEDs per cell
10 warm white LEDs (5 series × 2 parallel)
Multiplexing
Row–column scheme, 8.33 kHz refresh
Controller
Arduino Nano, 16 MHz
Power
15 V / 4 A, max 38.4 W, short-circuit protected
Diffusion
Frosted glass + paper layer for uniform illumination
Pieces
Transparent plastic (amber-tinted for black pieces)
github.com/allita99/8x8-LED-Matrix-Control-Circuit

## Slide 6
Board State Mechanism
PC computes legal moves from current board state
Transmits 64-bit hex activation mask via UART (57,600 baud rate)
Each bit = one board square
Only set bits are illuminated and classified
FBCCA evaluates only active-square frequencies
Dynamic frequency-to-square remapping at every move
Deselect option (origin square) enables error correction
Illegal moves are excluded by construction, never stimulated, never selected
Active targets (legal moves only)

## Slide 7
Signal Acquisition And Frequency Selection
EEG Acquisition
Amplifier: g.USBamp (Guger Technologies)
Channels: PO7, PO3, POz, PO4, PO8, O1, Oz, O2 (10-10 system)
Reference: Cz | Ground: AFz
Impedance: < 5 kΩ
Sampling rate: 512 Hz
Frequency Selection
28 optimized frequencies
Min. 0.1 Hz diff. between each harmonics
Filter-Bank CCA
Six sub-bands spanning [fn, 95 Hz]
fn ∈ {9.5, 21, 32.5, 44, 55.5, 67} Hz
Sine/cosine references up to the 5th harmonic per active frequency

## Slide 8
Confidence-Gated Selection & Legality Masking
Decision Rule
Argmax over, active frequencies
Accept only if confidence > threshold
Threshold Calibration
Set on noise input: raised until no selection fired for > 2 min
Conservative operating point suppresses false selections
Tuned in a narrow range per session (threshold lowered if no selection > ~30 s)
Deselect option (origin square) enables error correction

## Slide 9
Participants and Experiments
Participants (N = 6)
4 male, 2 female; mean age 24.67 ± 1.37 years
All self-reported no neurological/psychiatric conditions
Written consent (Declaration of Helsinki)
Ethics: Univ. Duisburg-Essen (24-11957-BO)
100% prior BCI experience; 50% had an official chess rating
Mean chess skill: 3.33 ± 1.21 (1–6 scale)
Trial Procedure
Puzzle display & mental-solving (≤ 2 min)
EEG stabilisation (~8 s)
Piece selection via SSVEP (confidence-thresholded)
Target square selection via SSVEP
Move executed; board manually updated
Adaptive threshold adjustment on repeated errors

## Slide 10
Performance Results
92.7%
Mean Operational Accuracy
95% CI: [85.8, 99.6] | SD = 0.066
[85.8–99.6]%
95% Confidence Interval
n = 6 participants
1m 42s
Mean Puzzle Completion Time (est.)
Including amp startup, board updates, UNDO
Chart: 
| P1 | P2 | P3 | P4 | P5 | P6
Operational Accuracy (%) | 97 | 94 | 89 | 95 | 93 | 88

## Slide 11
Questionnaire Results Summary
Fatigue increase: 3.17 ± 1.72 (moderate)
Flickering discomfort: 2.33 ± 1.37 (low–moderate)
Gaze control difficulty: 2.33 ± 1.21 (moderate)
Selection accuracy: 1.83 ± 0.41 (very positive)
Future applicability: 2.00 ± 1.55 (positive)

## Slide 12
Discussion
Performance
High accuracy across participants; dynamic legality masking reduced simultaneous classifier candidates
Direct register manipulation required for reliable LED multiplexing — Arduino's default I/O too slow
Active set reduced to 28 frequencies (from 64) to avoid harmonic overlap in usable SSVEP range
Limitations
Small sample size (N=6)
Flickering LEDs brightness/contrast
ITR not reported - Variable target set
Physical piece movement not autonomous

## Slide 13
Conclusion
Objective:
Presented an SSVEP-driven chess puzzle BCI on an illuminated physical chessboard
Combined LED stimulation, transparent chess pieces, FBCCA decoding, and chess-rule-constrained dynamic target allocation
Future Goals:
Larger user studies and novice participants
Robotic arm to automate physical piece movement
Higher brightness LED stimulation; improved diffusion
Stimulus parameter optimisation to reduce visual fatigue

## Slide 14
https://bci-lab.hochschule-rhein-waal.de
Our Team
Projects
Tools
List of publications
Contacts
https://bci-lab.hochschule-rhein-waal.de
Our Team
Projects
Tools
List of publications
Contacts
Atilla Cantürk Ivan Volosyak
Thank You – Q & A

## Slide 15
References
Ahn, M., Lee, M., Choi, J., & Jun, S. (2014). A review of brain-computer interface games and an opinion survey. Sensors, 14(8), 14601–14633.
Cattan, G. (2021). The use of brain–computer interfaces in games is not ready for the general public. Frontiers in Computer Science, 3.
Chen, X., Wang, Y., Gao, S., Jung, T.-P., & Gao, X. (2015). Filter bank canonical correlation analysis for implementing a high-speed SSVEP-based BCI. Journal of Neural Engineering, 12(4), 046008.
Choi, J. W., Rho, E., Huh, S., & Jo, S. (2018). An EOG/EEG-based hybrid brain-computer interface for chess. IEEE SMC, 129–134.
Hübner, D., Schall, A., & Tangermann, M. (2019). Two player online brain-controlled chess. IEEE EMBC, 3018–3021.
Hübner, D., Schall, A., & Tangermann, M. (2020). Unsupervised learning in a BCI chess application. Brain-Computer Interfaces, 7(1–2), 22–35.
Ladouce, S., Darmet, L., Torre Tresols, J. J., Velut, S., Ferraro, G., & Dehais, F. (2022). Improving user experience of SSVEP BCI through low amplitude depth and high frequency stimuli design. Scientific Reports, 12(1).
Leite, H. M. d. A., et al. (2018). Analysis of user interaction with a BCI based on SSVEP: case study of a game. Computational Intelligence and Neuroscience, 2018.
Toersche, H. A. (2007). Designing a brain-computer interface to chess. Twente Student Conference on IT.
Zhu, D., Bieger, J., Garcia Molina, G., & Aarts, R. M. (2010). A survey of stimulation methods used in SSVEP-based BCIs. Computational Intelligence and Neuroscience, 2010.
Icons
https://www.flaticon.com/free-icon/robot-arm_9791676?term=robot+arm&page=1&position=2&origin=search&related_id=9791676
https://www.flaticon.com/free-icon/chess_4363795?term=chess+board&page=1&position=2&origin=tag&related_id=4363795
https://www.flaticon.com/free-icon/diagram_14008539?term=amplifier&page=1&position=10&origin=search&related_id=14008539
https://www.flaticon.com/free-icon/chess_9568838?related_id=9568838
Icons from Font Awesome 6 Free (flask, chess-knight, stopwatch), by Fonticons, Inc., licensed under CC BY 4.0 (https://creativecommons.org/licenses/by/4.0/). Accessed via the react-icons package (MIT). https://fontawesome.com/license/free