## Slide 1: Single-Stimulus SSMVEP for EEG Biometrics: An Identification Study
Ayas Kiser, Alexander Szameitat and Ivan Volosyak
Rhine-Waal University of Applied Sciences · Snap GmbH
Notes: Good morning, everyone, and thank you for joining this presentation. My name is Ayas Kiser. Today, I will present our study, "Single-Stimulus SSMVEP for EEG Biometrics: An Identification Study." This work was carried out with Alexander Szameitat and Ivan Volosyak. Our main question was: can the brain response to one motion-based visual stimulus provide enough information to identify a person?
I will begin with explaining why EEG is interesting for biometric identification.

## Slide 2
Why EEG Biometrics?
EEG biometrics identifies a person from the brain’s own response, a trait that is internal, dynamic and hard to observe or replicate.
Subject
EEG response
Identity
Conventional biometrics
Fingerprint, iris patterns, facial features, ID cards, passwords, and signatures
Externally observable and potentially vulnerable to imitation, theft or forgery
EEG based biometrics
Non-invasive measurement of the brain’s electrical activity
Contains dynamic patterns linked to individual neurophysiology
Difficult to observe or reproduce externally
Resting state
Easy to acquire, but provides limited control over the elicited activity.
P300
Stimulus-locked and repeatable, but requires oddball protocols and longer recordings.
Motor imagery
Produces task-related cortical patterns, but requires training and shows substantial variability.
VEP
Frequency-locked, reproducible, and strongly represented over the occipital cortex.
Zhang et al. (2021); Beyrouthy et al. (2024); Thorpe et al. (2005); Akbarnia & Daliri (2024)
Common EEG paradigms for biometric identification
Notes: Most common biometric methods use visible or transferable information, such as a fingerprint, a face, or a password. These may be copied, stolen, or observed. EEG is different because it measures electrical activity inside the brain. This activity changes over time and is difficult to copy from outside the body. For a signal to be useful for identification, it must differ between people and be reasonably repeatable within the same person. EEG is a possible source, but it also changes with attention, tiredness, task, and recording conditions. We therefore gave every participant the same visual input and asked whether the evoked EEG still differed systematically between people. This tests short-term participant discriminability, not long-term security or real-world authentication.
This motivation leads to the difference between flicker-based and motion-based visual stimulation.

## Slide 3
Xie et al. (2012); Chai et al. (2019); Stawicki & Volosyak (2020); Azadi Moghadam & Maleki (2023); Yan et al. (2017); Karimi et al. (2022);
From Flicker to Motion
Conventional SSVEP
Periodic luminance modulation
Frequency-locked occipital response
Widely used in multi-target BCIs
Repetitive flicker may cause discomfort
Motion-based SSMVEP
Periodic motion without explicit on–off flicker
Frequency-locked steady-state response
Continuous spatial transformation
Favourable comfort outcomes reported
The gap: SSVEP and SSMVEP are extensively studied for command decoding. Their application to biometric identification, motion-based stimulation in particular, remains comparatively underexplored.
Notes: A conventional SSVEP uses repeated changes in brightness. It creates a clear EEG response at the stimulation frequency, but the flicker may be uncomfortable. A steady-state motion visual evoked potential, or SSMVEP, uses periodic motion instead of clear on-and-off flicker. Earlier work suggests that this can reduce the burden of obvious flicker. Most SSVEP and SSMVEP studies classify frequencies or commands; far fewer ask whether the responses differ reliably between people. In our study, the class labels are therefore participant identities, not stimulus frequencies.
From this research gap, we defined three questions for the present study.

## Slide 4
Study Overview
Research aim: To evaluate whether EEG responses elicited by a single, centrally presented motion stimulus contain sufficient subject-specific information for closed-set identification.
1
Configurable three-layer radial-motion stimulus
A motion-based stimulus with controllable inter-layer phase relationships, enabling synchronous and phase-shifted contraction-expansion patterns without explicit on-off flicker.
2
Controlled single-target paradigm
All participants viewed the same centered stimulus; only the stimulation frequency and inter-layer motion configuration varied, while target location and spatial attention remained unchanged.
3
Subject identification
Closed-set identification of eight participants was evaluated across stimulus configurations, frequencies, and preprocessing bandwidths using EEGNetSSVEP.
Notes: We examined three scientific questions. First, can one central SSMVEP target support identification of eight known participants across two short sessions? Second, does the motion configuration affect performance? Third, is participant information limited to a narrow band around the stimulation frequency, or present across a wider EEG band? Every participant viewed the same target location, both motion configurations, and all four frequencies. We evaluated the data with EEGNetSSVEP.
At the next slide I will first show how the two motion configurations differ.

## Slide 5
Stimulus Design
Stimulation 1
Stimulation 2
Stimulus 2 : Adjacent layers are progressively rotated relative to one another, creating a sequential contraction-expansion pattern. The dots remain continuously visible, with no on–off flicker. Both configurations were presented at 4, 6, 10, and 15 Hz.
Stimulus 1 : All three layers contract and expand synchronously.
Notes: Here you can see the experimental manipulation. In Stimulus One, all three layers contract and expand together. In Stimulus Two, neighboring layers are offset in time, so the motion progresses sequentially across them. The dots remain continuously visible in both cases. Therefore, the manipulation changes the timing of the motion rather than introducing simple on-and-off flicker. We tested both configurations at four, six, ten, and fifteen Hertz, allowing us to compare the effects of stimulus design and frequency.
I will now describe the participants, recording system, and session structure.

## Slide 6
Experimental Setup
Acquisition
g.USBamp amplifier (g.tec), 16 channels at 256 Hz
Passive Ag/AgCl electrodes (EasyCap) with abrasive gel
Electrode impedances kept below 5 kΩ
Stimulus presentation
Dell U2312HM, 1920 × 1080 at 60 Hz refresh
Viewing distance ≈ 60 cm, stable posture and gaze
Participants
8 right-handed participants - 4 female, 4 male
Mean age 25.25 years (range 20-30)
4 required visual correction; 6 had prior BCI experience
Ethics approval Univ. Duisburg-Essen; written informed consent
Procedure
Two recording sessions, separated by 20 min
Brief questionnaires administered before and after recording
Typical protocol duration: ~2 hours (including participant preparation and filling questionnaire forms)
Notes: We recorded from sixteen occipital and parieto-occipital EEG channels at 256 Hertz using a g.USBamp amplifier and passive electrodes. The stimulus was shown on a 60-Hertz monitor from about sixty centimeters away. Eight right-handed adults took part: four women and four men, with a mean age of about twenty-five. They completed two sessions about twenty minutes apart and brief questionnaires before and after recording. A typical visit, including EEG preparation and the forms, lasted about two hours. The short gap tests immediate session transfer, not long-term stability.
Within each recording session, all participants followed the same trial protocol.

## Slide 7
Experimental Protocol
2 Sessions
≈ 20 min apart
2 Blocks
Stimulus 1, then 2
4 Runs
4, 6, 10, 15 Hz
12 Trials
per run
Trial structure
2 s rest
Only one centrally located stimulus was displayed at a time, so target location, competing visual input and shifts in spatial attention stayed matched. The same stimulus and frequency order was used for every participant and session.
Questionnaires: Demographics, vision, prior BCI experience, tiredness, sleep and recent substance consumption beforehand; tiredness, eye discomfort, mental effort, motion perception, willingness to use and barriers afterwards.
7 s stimulation
Notes: Each session contained two blocks: Stimulus One was always presented first, followed by Stimulus Two. Each block had four frequency runs with twelve trials each. This gives forty-eight trials per stimulus, ninety-six per session, and one hundred ninety-two per participant. Each trial had two seconds of rest and seven seconds of stimulation. The order was fixed for everyone. The questionnaires covered background, sleep, and baseline tiredness before the experiment, then tiredness, eye discomfort, mental effort, usability, and practical barriers afterward.
After data collection, the EEG passed through the following preprocessing and evaluation pipeline.

## Slide 8
Analysis Pipeline
EEG
16 ch 256 Hz
Band-pass
2–32 Hz / ±4 Hz
Bad channels
Interpolate
EEGNetSSVEP
Snap Brain Toolbox
Subject ID
8 classes
Analysis 1 — Stimulus comparison
Stimulus 1 and Stimulus 2 evaluated separately
Two-fold cross-session
Performance averaged over both validation directions
Wideband 2-32 Hz band-pass; all 8 classes in both folds
Analysis 2 — Frequency-specific
One model per frequency × preprocessing setting
Validation: Stimulus 2 / Session 2, held out entirely
Training: all remaining recordings
Narrowband ±4 Hz vs. wideband 2-32 Hz
Notes: The analysis began with one sixteen-channel EEG trial. We compared two filter settings: a wide band from two to thirty-two Hertz, and a narrow band extending four Hertz below and above the tested frequency. Bad channels were found with MNE-Python's Local Outlier Factor method, using Euclidean distance, neighbors, and a threshold of one point five. Flagged channels were interpolated, and no additional preprocessing was applied. The data were then classified with EEGNetSSVEP. Analysis One compared the two motion configurations separately: we trained on one session, tested on the other, reversed the direction, and averaged the two results. Analysis Two examined each frequency and filter setting separately. Here, Stimulus Two from Session Two was the test set, while the remaining recordings formed the training set. This second analysis is therefore frequency-specific, but it is not a session holdout.
Before presenting the results, I will explain exactly what the classifier predicts.

## Slide 9
How was participant identification performed?
At validation time, the model receives EEG segment without a claimed identity and assigns it to one of the eight known participant classes.
All participants viewed the same single stimulus at 4, 6, 10 or 15 Hz.
16 channels 2-32 Hz filtering and automatic bad-channel detection
Training: The neural network learns participant-specific EEG patterns. Each participant represents one output class.
Validation: The participant class with the highest model score is selected.
EEGNetSSVEP Classification
Lawhern et al. (2018)
Notes: Identification was formulated as an eight-class, closed-set classification problem, with one class for each participant. At test time, the model received one preprocessed EEG segment without a claimed identity and assigned it to one of the eight known participant classes. EEGNetSSVEP is a compact convolutional network. Temporal filters learn repeating signal patterns, and spatial filters combine information across electrodes. The final layer produces eight scores; the highest determines the predicted identity. The model does not predict frequency and cannot reject an unknown person. Cross-session accuracy therefore measures short-term transfer only among these eight known participants.
Using this identification procedure, we first compared the two motion configurations.

## Slide 10
Results - Stimulus Comparison
Stimulus 1
94.96 %
accuracy · macro-F1 95.53 %
Stimulus 2
86.78 %
accuracy · macro-F1 85.99 %
Where Stimulus 2 loses
Class 3 recall falls to 36.6 %, split almost evenly between class 1 (31.3 %) and class 5 (31.6 %). All remaining classes stay above 84 %.
Stimulus 1: Errors concentrate in class 6 (recall 76.6 %, taken for class 2 in 11.6 % and class 1 in 5.9 % of its samples); every other class reaches at least 96.5 %. Classes 7 and 8 stay above 99.5 % under both configurations. Training accuracy: 99.55 % / 99.38 %.
At this study, identification is an eight-class problem in which class k corresponds to Participant k.
Notes: We report both accuracy and macro F one score. Accuracy is the overall percentage of correct predictions. Macro F one first calculates an F one score for each participant and gives all eight equal weight. Stimulus One reached ninety-four point nine six percent accuracy and a macro F one score of ninety-five point five three percent. Stimulus Two reached eighty-six point seven eight percent accuracy and a macro F one score of eighty-five point nine percent. Most of this difference came from Participant Three, whose recall under Stimulus Two was thirty-six point six percent. The other participants remained above eighty-four percent. The result therefore shows a participant-specific failure, not a uniform decrease for Stimulus Two. The stimulus difference should therefore be interpreted descriptively.
We then asked how the retained frequency range affected identification.

## Slide 11
Results - Bandwidth & Frequency
Validation accuracy per stimulation frequency.
Wideband 2–32 Hz
98.19 – 99.25 %
At every frequency. Macro-F1 98.08–99.23 %; the lowest class-level recall is 90.1 % (class 2 at 15 Hz).
Narrowband ±4 Hz
71.50 → 92.38 %
Rises steadily from 4 to 15 Hz. Macro-F1 climbs 72.36 → 90.19 %.
Narrowband failures are participant-specific at 4 Hz, 377 of 576 class-7 samples (65.5 %) are taken for class 8 (recall 34.5 %); at 6 Hz class 1 falls to 37.8 %. Harmonics generally lie outside the corresponding narrowband windows, and stimulation frequency and passband location vary together, so their contributions cannot be separated here.
Notes: The filter comparison produced a second clear pattern. With the wide two-to-thirty-two-Hertz band, accuracy ranged from ninety-eight point one nine to ninety-nine point two five percent across the four frequencies. With the narrow frequency-centered band, accuracy rose from seventy-one point five percent at four Hertz to ninety-two point three eight percent at fifteen Hertz. Participant information may therefore extend beyond the fundamental frequency; harmonics and broader signal patterns may contribute. However, the wide band may also retain information related to recording conditions, and Analysis Two was not a strict session holdout. The scientific conclusion is limited: performance depended strongly on bandwidth, but this experiment does not isolate the physiological source of the information.
Performance was only one outcome, so we also examined participant experience.

## Slide 12
Current SSMVEP Study
Questionnaire Results
3.1 → 4.37
tiredness, before → after
3.5 / 6
eye discomfort
3.25 / 6
mental effort
Reported barriers (multiple answers permitted)
Discomfort associated with the EEG equipment - 5 of 8
Setup time or complexity - 5 of 8
Concerns about brain-data privacy and storage - 3 of 8
All other barriers - one or two participants each
2.43 → 4.19
tiredness, before → after
3.76 / 6
eye discomfort
3.43 / 6
mental effort
Ratings were broadly comparable to the previous SSVEP study, with slightly lower eye discomfort and mental effort
Tiredness increased in both studies. Despite higher baseline tiredness in the current SSMVEP sample, the increase was smaller than in the previous SSVEP study (+1.27 vs. +1.76). Post-experiment ratings were comparable (4.37 vs. 4.19).
Previous SSVEP Study
Notes: The questionnaires were included as a secondary feasibility measure. On the six-point scale, mean tiredness increased from three point one before the experiment to four point three seven afterward. Mean eye discomfort was three point five, and mental effort was three point two five. Five participants selected EEG-equipment discomfort, and five selected setup time or complexity, as barriers. Three selected concerns about brain-data privacy and storage. Ratings were broadly similar to our earlier flicker-based study, but the participants differed and this group started more tired. With only eight participants, these comparisons are descriptive, not inferential.
Taken together, the performance and questionnaire data support four interpretations.

## Slide 13
Discussion
Participant differentiation
Participants could be distinguished during the same controlled visual task.
This suggests participant-related structure in the evoked EEG.
Short-term session transfer
Part of this structure transferred between sessions separated by 20 minutes.
Strict session-holdout validation is still needed.
Practical considerations
Participants reported their level of tiredness, eye discomfort, and mental effort.
Motion-based stimulation did not remove preparation, equipment, fatigue, or privacy concerns.
Stimulus and bandwidth effects
Performance varied with motion pattern and filter bandwidth.
Fixed stimulus order and different evaluation splits limit causal interpretation.
Notes: The evidence supports four interpretations. First, people could be distinguished during the same controlled visual task, suggesting participant-related structure in the evoked EEG. Second, part of this structure transferred between sessions separated by about twenty minutes. Third, performance changed with both motion pattern and filter bandwidth. However, the fixed stimulus order and the different evaluation split in Analysis Two prevent a simple causal conclusion. Fourth, the questionnaires show that a motion-based stimulus does not remove the practical burden of EEG preparation, equipment discomfort, fatigue, and data-privacy concerns.
These interpretations also show where the present evidence remains limited.

## Slide 14
Limitations & Future Work
Limitations
Sessions separated by only ≈ 20 minutes, too short to assess long-term biometric stability
Session-specific factors (impedance, cap placement, recording noise) may contribute, especially under wideband preprocessing
Only eight participants were recruited
Only two motion configurations, evaluated under controlled laboratory conditions
Descriptive comparisons only - no participant-level inferential testing
Future work
Counterbalance the order of the two stimulus configurations
Separate the recording sessions by days or weeks and apply a strict session holdout
Recruit larger and more diverse participant samples
Sweep further motion parameters: phase step, contraction range, number of layers
Apply predefined statistical comparisons with appropriate estimates of uncertainty
Notes: The study is a proof of concept and has several important limitations. There were only eight participants. Sessions were only twenty minutes apart, so we cannot claim long-term biometric stability. The frequency analysis was not a strict session holdout, and comparisons were descriptive, without formal participant-level tests. The closed-set model must choose one of the eight known people and cannot reject an impostor. Future work should use a larger and more diverse sample, counterbalance the stimulus order, separate sessions by days or weeks, apply a strict session-based split, predefine statistical tests, and evaluate open-set rejection.
With those limits in mind, I will state the conclusion at the appropriate level.

## Slide 15
Conclusion
EEG recorded during motion-based SSMVEP stimulation carries subject-related information relevant to closed-set identification over short intervals.
Synchronous motion reached 94.96 % cross-session accuracy versus 86.78 % for the phase-shifted configuration.
Wideband preprocessing reached 98.19–99.25 % at every frequency, while narrowband climbed 71.50 → 92.38 % from 4 to 15 Hz.
Motion-based SSMVEP is a promising, flicker-free basis for EEG-based biometric identification.
These are descriptive findings. Confirmation requires larger participant samples, longer inter-session intervals and participant-level statistical analysis.
Acknowledgment. Funded by the European Union’s research and innovation programme under the Marie Skłodowska-Curie grant agreement No 101118964. The authors thank Snap GmbH for the Snap Brain Toolbox experimental environment and EEG processing pipeline.
Notes: In conclusion, this study provides proof-of-concept evidence that motion-evoked EEG contains information that can distinguish eight known participants over a short interval. In the strict cross-session stimulus comparison, the together-moving pattern reached ninety-four point nine six percent accuracy, and the offset pattern reached eighty-six point seven eight percent. In the separate frequency analysis, the wider band performed better, but it used a different, less strict split; its values should not be compared directly with the cross-session results. The correct conclusion is short-term closed-set identification feasibility. It is not yet evidence of long-term stability, impostor rejection, or a deployable authentication system. Those questions require larger and longer studies with stricter controls.
The next slide provides the complete references used in the presentation.

## Slide 16
References
Beyrouthy, T., Mostafa, N., Roshdy, A., Karar, A. S., & Alkork, S. (2024). Review of EEG-based biometrics in 5G-IoT: Current trends and future prospects. Applied sciences, 14(2), 534.
Zhang, S., Sun, L., Mao, X., Hu, C., & Liu, P. (2021). Review on EEG‐Based Authentication Technology. Computational intelligence and neuroscience, 2021(1), 5229576.
Thorpe, J., Van Oorschot, P. C., & Somayaji, A. (2005, September). Pass-thoughts: authenticating with our minds. In Proceedings of the 2005 workshop on New security paradigms (pp. 45-56).
Akbarnia, Y., & Daliri, M. R. (2024). EEG-based identification system using deep neural networks with frequency features. Heliyon, 10(4).
Chai, X., Zhang, Z., Guan, K., Liu, G., & Niu, H. (2019). A radial zoom motion-based paradigm for steady state motion visual evoked potentials. Frontiers in Human Neuroscience, 13, 127.
Karimi, R., Mohammadi, A., Asif, A., & Benali, H. (2022). DF-SSmVEP: Dual frequency aggregated steady-state motion visual evoked potential design with bifold canonical correlation analysis. Sensors, 22(7), 2568.
Azadi Moghadam, M., & Maleki, A. (2023). Fatigue factors and fatigue indices in SSVEP-based brain-computer interfaces: A systematic review and meta-analysis. Frontiers in Human Neuroscience, 17, 1248474.
Stawicki, P., & Volosyak, I. (2020). Comparison of modern highly interactive flicker-free steady state motion visual evoked potentials for practical brain–computer interfaces. Brain Sciences, 10(10), 686.
Yan, W., Xu, G., Li, M., Xie, J., Han, C., Zhang, S., Luo, A., & Chen, C. (2017). Steady-state motion visual evoked potential (SSMVEP) based on equal luminance colored enhancement. PLOS ONE, 12(1), e0169642.
Xie, J., Xu, G., Wang, J., Zhang, F., & Zhang, Y. (2012). Steady-state motion visual evoked potentials produced by oscillating newton's rings: implications for brain-computer interfaces. Plos one, 7(6), e39707.
Lawhern, V. J., Solon, A. J., Waytowich, N. R., Gordon, S. M., Hung, C. P., & Lance, B. J. (2018). EEGNet: a compact convolutional neural network for EEG-based brain–computer interfaces. Journal of neural engineering, 15(5), 056013.
Notes: This slide lists the full references for the scientific background, stimulus designs, preprocessing tools, and EEGNetSSVEP method.

## Slide 17
Thank you !
Do you have any questions?
ayas.kiser@hochschule-rhein-waal.de
BCI Kleve - Brain-Computer Interface research lab
ivan.volosyak@hochschule-rhein-waal.de
BCI Kleve - Brain-Computer Interface research lab
alexander.szameitat@snap-gmbh.com
Snap GmbH
Notes: Thank you very much for your attention. I would also like to thank my co-authors, Alexander Szameitat and Ivan Volosyak, as well as the project partners and funders. I am happy to answer your questions.