## Slide 1
Reliable Asynchronous Control in MI BCIs:
An Unsupervised Spatial Focalisation Gating for Intentional Non-Control
Paolo Forin · Stefano Tortora · Emanuele Menegatti · Luca Tonin
Department of Information Engineering, University of Padua, Italy · Padova Neuroscience Center
paolo.forin@phd.unipd.it
WORKSHOP ON BRAIN-MACHINE INTERFACES IEEE SMC 2026 October 4-7, 2026

## Slide 2
MOTIVATION
The INC Problem in MI-BCI
BCI system are based on trials, specially BCI-MI based system where the user has to perform an imagination task.
Standard synchronous calibration assumes a stable Intentional Control (IC) state and assigns one static label to every time point of the trial.
But sustained attention is rarely constant: fatigue, mind-wandering and delayed initiation inject Intentional Non-Control (INC) / idling inside the “active” trial.
IEEE SMC 2026 · Bellevue, WA, USA
2
Unintended command fires
Integrator held at neutral
ONE TRIAL
IC
INC
IC
INC
IC
INC
time
IC — focused (informative)
INC — idling / mind-wandering (mislabeled noise)
A noisy-labelling problem: the classifier learns boundaries from data where some samples are background noise, diluting separability and decoding accuracy.

## Slide 3
materials and methods: OUR APPROACH
Spatial Focalisation Gating (SFG)
Hypothesis: genuine motor imagery produces a focal ERD of sensorimotor activity, compared with the diffuse power pattern of Rest/Intentional Non-Control (INC).
Spatial focality
feature F(t)
→
Unsupervised classifier
P(IC | F(t))
→
Training-set cleaning
Only gated, IC-consistent samples are used to fit the classifier.
IEEE SMC 2026 · Bellevue, WA, USA
4
Online reliability weighting
P(IC) continuously re-weights the integrator.

## Slide 4
materials and methods: NEW FEATURE
Spatial Focality
Why this feature?
Genuine MI produces a focal, contralateral ERD; rest is diffuse, high-power synchronisation.
IEEE SMC 2026 · Bellevue, WA, USA
7
Sensorimotor ROIs
Left
C3, C1, CP1
Centre
Cz, FCz, CPz
Right
C4, C2, CP2
Focality feature:
Rest: median ≈ min → F(t) ≈ 0
Tasks: median > min → F(t) high
F(t) = log( )
median( Pᴿᴼᴵ )
min( Pᴿᴼᴵ )
1) Spatial
F(t) compares power across the ROIs at one instant (not power now vs. Baseline). ERD lowers power only in the active ROI.
2) Class-agnostic
the min operator finds the active hemisphere automatically, without prior task knowledge.
3) Drift-robust
normalising against global power resists fatigue or impedance changes.
Select Region of Interests (ROIs) and compute the mean power Pᴿᴼᴵ

## Slide 5
materials and methods: UNSUPERVISED CLASSIFIER
The GMM Gate: Unsupervised Intent Detection
• A Gaussian Mixture Model (K = 2) is fit to the normalised focality feature F(t) in two latent states: High Focus (IC) and Low Focus / Rest (INC).
• The cluster with the higher mean focality is automatically labelled IC.
• Offline, this posterior acts as a gate: only samples classified as IC are kept to train the classifier.
• Online, the posterior weighs how much to trust the BCI classifier's output at each instant.
IEEE SMC 2026 · Bellevue, WA, USA
8
Gating Policy
INC
IC
focality feature F(t) →
P(IC) = 0.5
discard
keep
Automatic. No manual pruning, no labels — the GMM removes non-informative idling from the training set on its own.
Spatial focality
feature F(t)
→
GMM classifier
P(IC | F(t))

## Slide 6
materials and methods: SETUP
Experimental Setup & Paradigm
IEEE SMC 2026 · Bellevue, WA, USA
5
5
healthy subjects
(age 26.5 ± 1.5)
Classifier: QDA
Classes: Both hands VS Both feet
TRIAL ORGANIZATION (cue-based synchronous paradigm)
16
Electrodes
reference: right earlobe
ground: AFz
Calibration: 3 runs, always-correct feedback
Evaluation: 2 runs, real feedback
ROIs:
[C3, C1, CP1], [Cz, FCz, CPz], [C4, C2, CP2]
512 Hz
System g.tec with
g.USBamp
30
online trials
10×2 MI + 10 rest
60
calibration trials
30 x 2 MI class

## Slide 7
materials and methods: PIPELINE
Processing Pipeline
Identical chain offline (calibration) and online (closed-loop)
Band-pass
8–13 Hz & 18–24 Hz
4th-order Butterworth
Hilbert
Instantaneous power envelope
Smoothing
Moving average, 1-s buffer
Classifiers
QDA and GMM
Artifact rejection
Threshold-based EOG (Fp1, Fp2) & EMG
Online: streamed at 16 Hz inside the ROS-Neuro middleware.
IEEE SMC 2026 · Bellevue, WA, USA
6
Band-pass
8–13 Hz & 18–24 Hz
4th-order Butterworth
CAR filter
FP1, FP2 excluded

## Slide 8
materials and methods: OFFLINE TRAINING
Offline Gated Control Architecture
IEEE SMC 2026 · Bellevue, WA, USA
9
Processing pipeline: CAR, μ/β band-pass, Hilbert power (xₜ)
Artifact Check
Compute Spatial Focality and classify it
F(t) and P(IC | F(t))
Train the BCI classifier
gate( F(t) ) =
{
Accepted if P(IC | F(t)) ≥ 0.5
Rejected otherwise
Filtered samples

## Slide 9
materials and methods: ONLINE CONTROL
Online Gated Control Architecture
Processing pipeline: CAR, µ/β band-pass, Hilbert power (xt)
Artifact Check
GMM Gate
P(IC | F(t))
Classifier Direction
P(Classifier | xₜ)
IEEE SMC 2026 · Bellevue, WA, USA
10
Reliability-Weighted Soft-Increment Integrator
Pmerged = P(IC) · P(Classifier) + ( 1 − P(IC) ) · 0.5
v(t) = min( 1, |Pmerged(t) − 0.5| · 2 · Kgain )
C(t+1) = C(t) + sign(Pmerged − 0.5) · |v(t)| / bs
INC (P(IC)≈0):
Pmerged≈ 0.5 → v(t) ≈ 0 → C(t+1) ≈ C(t)
Feedback Shown to the User

## Slide 10
results: OFFLINE
Isolating the Gate's Effect
Baseline architecture simulated on the same neural traces recorded under SFG.
Trial Accuracy:
comparable (p = 0.1055): both equally accurate once triggered
Timeout Rate:
comparable (p = 0.5117): gate doesn't impede execution
INC Accuracy:
76.0% vs 18.0% (p = 0.0059): a significant difference
IEEE SMC 2026 · Bellevue, WA, USA
12

## Slide 11
results: ONLINE
Closed-Loop Performance
24% → 76%
INC ACCURACY
p = 0.0020 **
8% → 16.5%
TIMEOUT RATE
deliberate safety trade-off
IEEE SMC 2026 · Bellevue, WA, USA
11
TRIAL ACCURACY
Without considering timeouts
> 90%

## Slide 12
results: ONLINE
Command Latency
INC, IC: Time to Miss
SFG requires more time before an unintended command fires.
IEEE SMC 2026 · Bellevue, WA, USA
13
+1.3s (p = 0.0645, n.s. Wilcoxon signed-rank).
IC: Time to Hit

## Slide 13
15
IEEE SMC 2026 · Bellevue, WA, USA
OUR
TRAD
results: ONLINE
Online Closed-Loop Control Performance

## Slide 14
CONCLUSION and TAKE-HOME MESSAGE
When the brain isn't focused, the system should know it.
An unsupervised, GMM-based Spatial Focalisation Gate turns spatial EEG focality into a real-time trust signal that decides whether the command is trustworthy enough to drive the external device.
LIMITATIONS
OUTLOOK
15
IEEE SMC 2026 · Bellevue, WA, USA
Restricted to a two-class paradigm.
Validated on a small cohort (5 subjects).
Proof of concept: validated within a synchronous, cue-based paradigm, not yet asynchronous.
Validate on larger, more diverse cohorts to confirm the effect beyond N=5.
Extend beyond motor imagery to other paradigms, e.g. CVSA (covert visual spatial attention).
Move from the synchronous, cue-based setting to real asynchronous, self-paced control.

## Slide 15
THANK YOU
Questions?
Reliable Asynchronous Control in MI BCIs: An Unsupervised Spatial Focalisation Gating for Intentional Non-Control
paolo.forin@phd.unipd.it
Paolo Forin · Stefano Tortora · Emanuele Menegatti · Luca Tonin
IEEE SMC 2026 · Bellevue, WA